## Slide 1: V283D-4G
1*XPON+4GE ONU
Introduction:
V283D-4G(XPON 4GE ONU) supports Dual mode(XPON), It can also be applied to a wide temperature environment, and also has a powerful firewall function.
V283D-4G(XPON 4GE ONU) meets telecom operators FTTO (office), FTTD (Desk), FTTH(Home) broadband speed, SOHO broadband access, video surveillance and other requirements and design a GPON/EPON Gigabit Ethernet products. The box is based on the mature Gigabit GPON/EPON technology, highly reliable and easy to maintain, with guaranteed QOS for different service. And it is fully compliant with technical regulations such as ITU-T G.984.x and IEEE802.3ah.SFP with SC/PC Connector Transceiver.
Key Features:
Application Chart:
XPON Dual Mode
Automatically Access to EPON/GPON
ZTE Chipset
High Performance Solution
Powerful Firewall
IPv4/IPv6 Dual Stack
SC/PC
OLT
SNMP
EMS
Spliter
Internet
RJ45
12V DC
PC
IPTV
Topset

## Slide 2
Product Name | Product Description | Accessories
V283D-4G | 4GE | AC-DC power adaptor: DC12V/0.5A
Dimension | 130mm*113mm*28mm(L*W*H)
Net weight | 0.148KG
Operating condition | Operating temp: 0 ~ +50°C Operating humidity: 5 ~ 90% (non-condensed)
Storing condition | Storing temp: -30 ~ +60°C Storing humidity: 5 ~ 90% (non-condensed)
Power adapter | DC 12V/0.5A, external AC-DC power adaptor
Power supply | ≤6W
Interfaces | 4GE
Indicators | PWR, PON, LOS, GE1, FE2~FE3
Hardware Parameter
PON interface | 1 XPON port(EPON PX20+ & GPON Class B+) SC single mode, SC/UPC connector TX optical power: 0～+4dBm RX sensitivity: -27dBm Overload optical power: -3dBm(EPON) or -8dBm(GPON) Transmission distance: 20KM Wavelength: TX 1310nm, RX1490nm
LAN interface | 4*GE, Auto-negotiation RJ45 connectors
Interface Parameter
XPON Mode | Dual mode,Auto-access to EPON/GPON OLT
Uplink Mode | Bridging and Routing Mode
Abnormal protection | Detecting Rogue ONU, Hardware Dying Gasp
Firewall | DDOS, Filtering Based on ACL/MAC/URL
Function Data
Basic | Support MPCP discover&register Support authentication Mac/Loid/Mac+Loid Support Triple Churning Support DBA bandwidth Support auto-detecting, auto-configuration, and auto firmware upgrade Support SN/Psw/Loid/Loid+Psw authentication
Alarm | Support Dying Gasp Support Port Loop Detect Support Eth Port Los
LAN | Support Port rate limiting Support Loop detection Support Flow control Support Storm control
VLAN | Support VLAN tag mode Support VLAN transparent mode Support VLAN trunk mode(max 8 vlans) Support VLAN 1:1 translation mode(≤8 vlans) Auto VLAN detection
Multicast | Support MLD Support IGMPv1/v2/Snooping Max Multicast vlan 8 Max Multicast Group 64
QoS | Support 4 queues Support SP and WRR Support 802.1P
L3 | Support IPv4/IPv6 Support DHCP/PPPOE/Static IP Support Static route Support NAT
Management | Support CTC OAM 2.0 and 2.1 Support ITUT984.x OMCI Support TR069/WEB/TELNET/CLI
Product Feature